ECT 213				Digital Circuits I	           		Lab 5

Simplification using Karnaugh Mapping

Parts List

| Part Name | Quantity needed |
| --- | --- |
| 1kΩ SIP | 1 |
| 330 Ω SIP | 1 |
| LED (Light Emitting Diode) | 1 |
| AND gate, 74LS08 IC | note |
| INVERTER, 74LS04 IC | note |
| NOR gate, 74LS02 IC | note |
| 3 Input NAND gate, 74LS11 | note |
| OR gate, 74LS32 IC | note |
| Input NAND gate , 74LS00 IC | note |
| Dip Switch (8 switches) | 1 |

Note:

- Quantity varies based on student design of circuit.

- Use GOOGLE to look up IC’s for power and ground connections.

- Given the following truth table

| Inputs | Output |
| --- | --- |
| A | B | C | X |
| 0 | 0 | 0 | 1 |
| 0 | 0 | 1 | 1 |
| 0 | 1 | 0 | 0 |
| 0 | 1 | 1 | 1 |
| 1 | 0 | 0 | 1 |
| 1 | 0 | 1 | 1 |
| 1 | 1 | 0 | 0 |
| 1 | 1 | 1 | 1 |

  - Determine the FULL Boolean equation.

  - Use HADES to draw the circuit for the original Boolean equation.

  - Submit the Hades simulation (.hds file) via online submission (Lab 5 -  cct 1) for credit.

  - On a printed copy of the HADES simulation, write the pin numbers for each gate. Wire Circuit on breadboard.  Demonstrate to the Instructor for credit.

  - Simplify the Boolean equation using Boolean rules, laws, and theorems.  Write all steps used to simplify.  Include the rules and laws used at each step.

Law 1: Commutative

Law 2: Associative

Law 3: Distributive

DeMorgan’s Theorem:

  - Fill in the following Karnaugh Map based of the original truth table.

  - Determine Most Simplified Boolean equation using filled in Karnaugh Map.

  - Draw simplified circuit using HADES. Submit the Hades simulation (.hds file) via online submission (Lab 5 -  cct 2) for credit.

  - On a printed copy of the HADES Schematic, place the pin number for each gate used. Wire simplified circuit on breadboard.  Demonstrate to instructor.

- Given the following logic circuit:

  - Determine the Boolean equation.

  - Determine the most simplified Boolean equations using Karnaugh mapping.

  - Design the circuit from the simplified expression above using HADES.  Submit the Hades simulation (.hds file) via online submission (Lab 5 -  cct 3) for credit.

  - On a printed copy of the HADES Schematic, show the pin numbers for each gate used. Wire circuit on breadboard.  Demonstrate to receive credit.

  - Turn in this paper (Along with the HADES schematics with pin numbers) to the instructor for credit (you are NOT required to submit this electronically).