Department of

Electronics, Computer, and Information Technology

ECT 213 Digital Electronics

Lecture 1:

Chapter 1:

Digital vs Analog Signals

Number Systems

Digital Signals

Analog vs Digital:

Analog:	continuous waveform.

Analog represents most 				     natural occurring physical

quantities.

Digital:	discrete levels in waveform.

High level represents ______

Low level represents ______

Analog vs Digital:

Each analog ___________ is represented by a ____________ of

digital _________ .

Analog vs Digital:

Advantages of Digital vs Analog.

__________ in signals are reduced.

Analog vs Digital:

Logic 1 represents high

Logic 0 represents low

Number Systems:  Decimal

Base 10

0

1

2

3

4

5

6

7

8

9

456710 = 4567

| 103 | 102 | 101 | 100 |
| --- | --- | --- | --- |
| 1000 | 100 | 10 | 1 |

Number Systems:  Binary

| Base 2 | Base 10 |
| --- | --- |
| 0 | 0 |
| 1 | 1 |
| 10 | 2 |

1100102 ≠ 110010

| 25 | 24 | 23 | 22 | 21 | 20 |
| --- | --- | --- | --- | --- | --- |
| 32 | 16 | 8 | 4 | 2 | 1 |

Convert from decimal to Binary

Method 1:	Using Weighting factor

Example 1:

Convert 100 to binary using weighting factors.

| 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |

Example 2:

Convert 200 to binary using weighting factors.

| 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |

Convert from decimal to Binary

Example 3:

Convert 100 to binary using division method.

| Division | Quotient | Remainder |
| --- | --- | --- |

Example 4:

Convert 200 to binary using division method.

| Division | Quotient | Remainder |
| --- | --- | --- |

Converting from binary to decimal.

Example 5:

10101102 to decimal

| 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |

Example 6:

Convert 110100102 to decimal

| 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |

Number system: Octal

| Base 8 | Base 10 | Base 2 |
| --- | --- | --- |
| 08 | 0 | 0002 |
| 18 | 1 | 0012 |
| 28 | 2 | 0102 |
| 38 | 3 | 0112 |
| 48 | 4 | 1002 |
| 58 | 5 | 1012 |
| 68 | 6 | 1102 |
| 78 | 7 | 1112 |
| 108 | 8 | 10002 |

Converting from octal to decimal:

Example 7:  658 to decimal

| 81 | 80 |
| --- | --- |
| 8 | 1 |

Example 8:  2258 to decimal

| 82 | 81 | 80 |
| --- | --- | --- |
| 64 | 8 | 1 |

Converting from decimal to octal:

Use the same methods as with binary.

1.	Weighted factors

2.	Divide by base

Example 9:  Convert 100 to Octal Using Weighted factors.

| 82 | 81 | 80 |
| --- | --- | --- |
| 64 | 8 | 1 |

Example 10:

Convert 221 to Octal Using Weighted factors.

| 82 | 81 | 80 |
| --- | --- | --- |
| 64 | 8 | 1 |

Example 11:

Convert 221 to Octal using division method.

| Division | Quotient | Remainder |
| --- | --- | --- |

Convert from Octal to binary.

2---- = 8

Example 12:   Convert 2748 to binary.

Binary to Octal Conversions

Example 13:   Convert 1011012 to Octal.

Example 14:  Convert 11001101012 to Octal.

Number Systems: Hexadecimal

| Base 10 | Base2 | Base 16 |  | Base 10 | Base2 | Base 16 |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0000 | 0 |  | 8 | 1000 | 8 |
| 1 | 0001 | 1 |  | 9 | 1001 | 9 |
| 2 | 0010 | 2 |  | 10 | 1010 | A |
| 3 | 0011 | 3 |  | 11 | 1011 | B |
| 4 | 0100 | 4 |  | 12 | 1100 | C |
| 5 | 0101 | 5 |  | 13 | 1101 | D |
| 6 | 0110 | 6 |  | 14 | 1110 | E |
| 7 | 0111 | 7 |  | 15 | 1111 | F |

Converting from Hexadecimal to decimal.

Example 15: Convert 7A16 to decimal.

| 161 | 160 |
| --- | --- |
| 16 | 1 |

Example 16: Convert 101016 to decimal.

| 164 | 163 | 162 | 161 | 160 |
| --- | --- | --- | --- | --- |
| 65536 | 4096 | 256 | 16 | 1 |

Convert from Hexadecimal to binary.

2 ---- = 16

Example 17: Convert BAD16 to binary

Convert from binary to Hexadecimal.

Example 18: Convert 1111001012 to hexadecimal.

Binary Coded Decimals

Decimal is represent by 4 binary digits

| Base 10 | Base 2 | BCD |
| --- | --- | --- |
| 0 | 00002 | 0000BCD |
| 1 | 00012 | 0001BCD |
| 2 | 00102 | 0010BCD |
| 3 | 00112 | 0011BCD |
| 4 | 01002 | 0100BCD |
| 5 | 01012 | 0101BCD |
| 6 | 01102 | 0110BCD |
| 7 | 01112 | 0111BCD |
| 8 | 10002 | 1000BCD |
| 9 | 10012 | 1001BCD |
| 10 | 10102 | 00010000BCD |
| 11 | 10112 | 00010001BCD |
| 12 | 11002 | 00010010BCD |
| 13 | 11012 | 00010011BCD |
| 14 | 11102 | 00010100BCD |
| 15 | 11112 | 00010101BCD |

Example 19:	Convert the following BCD number to Decimal.

10010111BCD to decimal.

Example 20:	Convert the following BCD number to Hexadecimal.

01111001BCD to Hexadecimal.

Example 21:	Convert the following BCD number to Binary.

01010111BCD to Binary

Example 22:	Convert the following Decimal number to BCD.

2006 to BCD.

Example 23:	Convert the following Octal number to BCD.     20068 to BCD

ASCII (pronounced “askee”) Code

- American Standard Code for Information Exchange

- Industry Standard for input/output (I/O) code

- 7-bit binary string to represent all alphanumeric data in for computer I/O

- 27 = 128 possible code groups

Example 24:	Use above table to convert the following to ASCII.

- #

- 0123 !

Example 25:	Use above table to convert the following to ASCII and add leading zero for each alphanumeric value.  List answer in hex.

- #

- 0123 !